## Slide 1: Application of Weighted Essentially Non-Oscillatory Limiting to Compact Interpolation Schemes
Debojyoti Ghosh
Graduate Research Assistant
Alfred Gessow Rotorcraft Center Aerospace Engineering Department University of Maryland, College Park
AIAA Region I Young Professional, Student, and Education Conference 2011
4th November, 2011, Johns Hopkins University / Applied Physics Laboratory Kossiakoff Center, Laurel, MD
James D. Baeder
Associate Professor

## Slide 2: Motivation and Objectives
Accurate numerical simulation of the wake flow field around a rotorcraft
Long term convection and mutual interaction of vortices
Interactions of vortices with fuselage and ground plane
High order accurate Navier-Stokes solver
Lower dissipation to preserve vortices as they convect over large distances
Smaller stencil for same order of accuracy to reduce data transfer costs for multiple-mesh solutions

## Slide 3: Introduction
Scalar hyperbolic partial differential equation
Discretization in time leads to an ordinary differential equation (solved by Euler explicit or TVD RK3)
Reconstruction – interpolation of f at the interfaces from the cell centered/averaged values
Upwinding – biased interpolation stencil to model wave nature of the solution

## Slide 4: Compact Schemes
High order accuracy with smaller stencils
Better spectral resolution than explicit interpolation
Lower dissipation at well-resolved frequencies
Taylor series error order of magnitude lower

## Slide 5: Compact-Reconstruction WENO Schemes
Convex combination of candidate r-th order accurate stencils
Weights of each stencil based on “smoothness” (measured by divided differences of the appropriate order)
Traditional WENO schemes use explicit interpolation
  Higher order accuracy  wider stencil  oscillatory solutions
Compact-Reconstruction (CRWENO) schemes constructed by using implicit interpolations as candidates in the WENO algorithm
  Advantages of compact interpolation schemes (smaller stencil, lower dispersion and dissipation, lower absolute errors)
  Non-oscillatory reconstruction across discontinuities
Optimal Weights
WENO Weights

## Slide 6: Example: CRWENO5

## Slide 7: Smoothness Indicators
Weights are calculated based on smoothness indicators of corresponding explicit stencils (same as WENO5 scheme)

## Slide 8: Linear Advection Equation
5th order convergence with lower absolute error than WENO5
Less smearing and clipping than WENO5

## Slide 9: Inviscid Burgers Equation
Initial sinusoidal solution turns into a shock wave (non-linear flux)
5th order convergence (before shock formation) with lower absolute error than WENO5

## Slide 10: Extension to the Euler Equations
Compressible Euler equations in 1D given by
In the form of a general hyperbolic PDE
Extension of interpolation schemes for scalar quantities to a system of equations
  Component-wise reconstruction of conservative variables (ρ, ρu, e)
  Reconstruction of primitive (flow) variables (ρ, u, p)
  Reconstruction of characteristic variables

## Slide 11: Characteristic-based Reconstruction
Characteristic based reconstruction respects the physics of the problem – 1D scalar wave propagation along each characteristic
i
i+1
Uavg (Roe averaged)
Eigenvalues, left and right eigenvectors
For interface j+1/2, characteristic quantities are given by
Reconstruct
Upwinding (Roe-Fixed)
Flux in conservative form

## Slide 12: CRWENO5 for 1D Euler Equations
Scalar interpolation scheme applied to the characteristic variables
Results in a block tri-diagonal linear system along each dimension (as compared to tri-diagonal system for component-wise reconstruction)
For multi-dimensions, solution of linear system required along each grid line
k = 1,2,3

## Slide 13: Entropy Wave
Smooth problem involving the convection of an entropy wave
  Density wave convects without dissipation, constant velocity and pressure
Exact solution given by
Periodic boundary conditions enforced on both boundaries
Solution compared after one pass over the domain
Errors and order of convergence compared
  Lower absolute errors for CRWENO5 at same order of convergence

## Slide 14: 1D Riemann Problems
Initial condition consists of two states separated by a thin partition
Initial discontinuity is decomposed into a rarefaction wave (RF), a contact discontinuity (CD) and a shock wave (S)
  Sod’s shock tube problem
  Lax’s shock tube problem
Benchmark cases for code validation
Require robust solvers to prevent spurious oscillations
RF
CD
S

## Slide 15: Sod’s Shock Tube
Comparison of different reconstruction methods
Comparison of WENO5 and CRWENO5
Characteristic – based reconstruction yields non-oscillatory results (though computationally more expensive)
Low dissipation of CRWENO5 results in sharper resolution of shock and contact discontinuity

## Slide 16: Lax’s Shock Tube
Oscillations caused by reconstruction of conservative and primitive variables
CRWENO5 shows less smearing of shock and contact discontinuity
Conservative Variable Reconstruction
Characteristic-based Reconstruction

## Slide 17: Shock-Entropy Interaction
Interaction between a shock wave and an entropy wave
  Solution contains discontinuity and high-frequency waves
Initial condition consists of right-moving shock and density wave
Extrapolation boundary conditions enforced on both boundaries
“Fine Grid Solution” obtained with WENO5 on 2000 point grid
CRWENO shows lower dissipation and clipping of high-frequency waves

## Slide 18: Isentropic Vortex Convection (Euler 2D)
Convection of an isentropic vortex on a periodic domain
Results shown for a 40x40 grid with WENO5 and CRWENO5
Lower dissipation of CRWENO5 preserves vortex for long–term convection
Y-Velocity after 1 cycles over the domain
Pressure after 1 and 5 cycles over the domain

## Slide 19: Conclusions and Future Work
Benefits of using the Compact-Reconstruction WENO scheme
  Smaller stencil for same order of convergence, lower absolute errors
  Lower dissipation leads to better resolution of discontinuities and better long-term convection properties
  Computational expense at same grid size is marginally more but coarser grids can be used for same error in solution
Characteristic vs. Component-wise reconstruction
  Characteristic reconstruction is costlier, even more so for implicit reconstruction schemes (block tri-diagonal solver)
  More robust since physically more accurate – non-oscillatory results for sharp discontinuities
  Results similar in case of smooth flows
Implementation of CRWENO for multi-dimensions
  2D and 3D Navier-Stokes solvers
  Application to airfoil cases, including pitching and plunging airfoils
  Simulation of flow field in a rotorcraft wake (convection and interaction of wake vortices)

## Slide 20: End